## Slide 1: CE101 Engineering Drawing Lec5: Projection of Planes
Indian Institute of Technology Guwahati
Notes: Note:
When it is given that a side is resting on a RP, then don’t think about the true length and top view inclinations
Think about them only when it is given that the plane is resting on the HP on a point

## Slide 2: Positions of Planes
Plane parallel to an RP
  Plane parallel to the HP
  Plane parallel to the VP
Plane inclined to one RP and perpendicular to the other RP
  Plane is inclined to the HP and perpendicular to the VP
  Plane is inclined to the VP and perpendicular to the HP
Plane perpendicular to both the RPs
Plane inclined to both the RPs (Oblique planes)

## Slide 3: Terms Used In Projections of Planes
True Length (TL): The actual length of a plane is called its true length.
Inclination with the HP (θp): It is the true angle that a plane makes with its projection on the HP. It is indicated by θp.
Inclination with the VP (Φp): It is the true angle that a plane makes with its projection on the VP. It is indicated by Φp.
Horizontal Trace (HT): The real or imaginary line of intersection of a plane with the HP is called the horizontal trace of the plane.
Vertical Trace (VT): The real or imaginary line of intersection of a plane with the VP is called the vertical trace of the plane.
Perpendicular Planes: The planes perpendicular to one or both the RPs.
Oblique Planes: Planes inclined to both the RPs
Line View or Edge View: The view of a plane seen as a line.

## Slide 4: Plane Parallel to An RP
FV
T V
For T.V.
Rectangular plane PARALLEL TO HP
VP
a’
d’
c’
b’
HP
a
b
c
d
A regular pentagon ABCDE of side 30 mm is parallel to the VP. The side AB is perpendicular to the HP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV

## Slide 5
HP
a1
b1
c1
d1
VP
VP
a’
d’
c’
b’
VP
a’
d’
c’
b’
FV-3
T V-3
For Fv
For Tv
FV-1
T V-1
For F.V.
For T.V.
For T.V.
For F.V.
HP
a
b
c
d
a1’
d1’
c1’
b1’
HP
a1
b1
c1
d1
FV-2
T V-2
RECTANGLE INCLINED TO BOTH PLANES– OBSERVE AND NOTE ALL STEPS
SURFACE PARALLEL TO HP
PICTORIAL PRESENTATION
SURFACE INCLINED TO HP
PICTORIAL PRESENTATION
ONE SMALL SIDE INCLINED TO VP
PICTORIAL PRESENTATION
ORTHOGRAPHIC
FV- TL of Long edge // to xy
TV-True Shape
ORTHOGRAPHIC
FV- TL of long edge Inclined to XY
TV- Reduced Shape, projected
ORTHOGRAPHIC
FV- Apparent Shape, projected
TV-Previous Shape, rotated
A
B
C

## Slide 6
When we rotate the plane such that its angle with the VP changes, kepping the angle with the HP constant , then TV is simply rotated

## Slide 7
X
Y
a
b
c
d
a’
b’
c’
d’
a1
b1
c1
d1
a1
b1
c1
d1
a’
b’
d’
c’
c’1
d’1
b’1
a’1
450
300
Problem 1:
Rectangle 30 mm and 50 mm sides is resting on HP on one small side which is 300 inclined to VP, while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------// to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y
drawing one small side vertical.
Surface // to HP
Surface inclined to HP
Side
Inclined
to VP

## Slide 8
X
Y
a
b
c
d
a’
b’
c’
d’
a1
b1
c1
d1
a1
b1
c1
d1
a’
b’
d’
c’
c’1
d’1
b’1
a’1
450
300
Problem 1b:
Rectangle 30 mm and 50 mm sides is resting on HP on one small side which is 300 inclined to VP, while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------// to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y
drawing one small side vertical.
Surface // to HP
Surface inclined to HP
Side
Inclined
to VP

## Slide 9
X
a
b
c
d
a1’
b1’
c’
d’
a’
b’
d1’
c1’
300
Problem 1c:
Rectangle 30 mm and 50 mm sides is resting on HP on one small side which is 300 inclined to VP, while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------// to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y
drawing one small side vertical.
Surface // to VP
Surface inclined to VP
a
b
c
d
We cannot rotate the plane 45º with the horizontal (HP), since we do not know how much shortening of sides would occur
Therefore, always start drawing the views by following the information about inclination of surface (Point 1), and assuming the surface is parallel to the specified Reference Plane (Point 2)

## Slide 10: Plane Inclined to One RP and Perpendicular to Other RP
Problem 2: A regular pentagon ABCDE of side 30 mm is inclined at 45o to the VP and perpendicular to the HP. The side AB is perpendicular to the HP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV
45
a1
b1
c1
e1
d1
a1’
b1’
c1’
d1’
e1’
Stage 1
Stage II
30
Side a’-b’ is
Perpendicular to HP
Projectors from
a’, b’, c’, d’, e’
Projectors from
a1, b1, c1, d1, e1
Point of
intersection

## Slide 11: Plane Inclined to One RP and Perpendicular to Other RP
X
Y
Problem 3: A regular pentagon of 25mm side has one side on the ground. Its plane is inclined at 45º to the HP and perpendicular to the VP. Draw its projections
a
b
c
d
e
25
a’e’
b’d’
c’
a’e’
b’d’
c’
a1
b1
c1
d1
e1
45º
Stage 1
Stage 2
One side
On the ground
One side
On the ground

## Slide 12: Plane Inclined to One RP and Perpendicular to Other RP
Problem 4: Draw the projections of a circle of 50 mm diameter having its plane vertical and inclined at 30º to the VP. Its centre is 30 mm above the HP and 20 mm in front of the VP.
X
Y
1’
2’
3’
4’
5’
6’
7’
8’
9’
10’
11’
12’
30
20
1
2, 12
3, 11
4, 10
5, 9
6, 8
7
1
2, 12
3, 11
4, 10
5, 9
6, 8
7
30º
41’
31’
51’
21’
61’
11’
71’
121’
81’
111’
91’
101’
50 Ø
Stage 1
Stage 2

## Slide 13
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? -------- any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
Problem 5:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides with it’s surface 450 inclined to HP.
Draw its projections when the side in HP makes 300 angle with VP
a’
b’
d’
b1
d
c1
a
c’e’
b
c
d1
b’1
a1
e’1
c’1
d’1
a1
b1
c1
d1
d’
a’
b’
c’e’
e1
e1
a’1
X
Y
450
300
e
SURFACE AND SIDE INCLINATIONS
ARE DIRECTLY GIVEN.

## Slide 14
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? -------- any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
Problem 5b:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides with it’s surface 450 inclined to HP.
Draw its projections when the side in HP makes 300 angle with VP
a’
b’
d’
b1
d
c1
a
c’e’
b
c
d1
b’1
a1
e’1
c’1
d’1
d’
a’
b’
c’e’
a1
b1
c1
d1
e1
e1
a’1
X
Y
450
300
e
SURFACE AND SIDE INCLINATIONS
ARE DIRECTLY GIVEN.

## Slide 15
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? -------- any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
Problem 5c:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides while it’s opposite vertex (corner) is 30 mm above HP.
Draw its projections when the side in HP makes 300 angle with VP
a’
b’
d’
b1
d
c1
a
c’e’
b
c
d1
b’1
a1
e’1
c’1
d’1
d’
a’
b’
c’e’
a1
b1
c1
d1
e1
e1
a’1
X
Y
300
e
SURFACE INCLINATION INDIRECTLY GIVEN
SIDE INCLINATION DIRECTLY GIVEN.
ONLY CHANGE is the manner in which surface inclination is described:
One side on HP & it’s opposite corner 30 mm above HP.
Hence redraw 1st FV as a 2nd FV making above arrangement.
Keep a’b’ on XY & d’ 30 mm above XY.
30

## Slide 16
A point resting on HP and a edge resting on HP are proceeded with two different methods.

## Slide 17: Plane Inclined to Both RPs
Problem 6: A regular pentagon ABCDE of side 30 mm has one of its edges parallel to the VP and inclined at 30o to the HP. The pentagon is inclined at 45o to the VP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV
45
a1
b1
c1
e1
d1
a1’
b1’
c1’
d1’
e1’
Stage 1
Stage II
30
a2’
b2’
c2’
d2’
e2’
30
a2
b2
c2
d2
e2
Stage III

## Slide 18: Plane Inclined to Both RPs
Problem 7: Draw the projections of a regular hexagon of 25 mm sides, having one of its side in the HP and inclined at 60o to the VP and its surface making an angle of 45º with the HP.
X
Y
a
b
c
d
e
f
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
f1
a1
c1
b1
d1
e1
45º
60º
a1’
b1’
c1’
d1’
e1’
f1’
Stage I: Plane parallel to HP
Stage II: Plane inclined to HP at 45°and ┴ to VP
Stage III: Side on the HP making 60° with the VP.
Notes: Always draw the hexagon as a benzene ring

## Slide 19
As 3rd step
redraw 2nd TV keeping
side DE on xy line.
Because it is in VP
as said in problem.
X
Y
a
b
c
d
e
f
Problem 8:
A hexagonal lamina has its one side in HP and
Its opposite parallel side is 25 mm above HP and
In VP. Draw it’s projections.
Take side of hexagon 30 mm long.
ONLY CHANGE is the manner in which surface inclination
is described:
One side on HP & it’s opposite side 25 mm above HP.
Hence redraw 1st FV as a 2nd FV making above arrangement.
Keep a’b’ on XY & d’e’ 25 mm above XY.
25
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
c1’
b’1
a’1
f’1
d’1
e’1
f1
a1
c1
b1
d1
e1
Notes: IMP question

## Slide 20
Problem 9:
A 300 – 600 set square of longest side
100 mm long, is in VP and 300 inclined
to HP while it’s surface is 450 inclined
to VP. Draw it’s projections
(Surface & Side inclinations directly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
c1
X
Y
300
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
c
a’1
b’1
c’1
c’
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
Surface // to VP
Surface inclined to VP
Side inclined to HP
Notes: The side which is given to be resting on a particular plane and making an angle of theta with the other plane.
Then, first of all draw that side perpendicular to the other plane in step 1 .(IMP)

## Slide 21
c
c1
X
Y
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
a’1
b’1
c’1
c’
35
10
Problem 9b:
A 300 – 600 set square of longest side
100 mm long is in VP and it’s surface
450 inclined to VP. One end of longest
side is 10 mm and other end is 35 mm
above HP. Draw it’s projections
(Surface inclination directly given.
Side inclination indirectly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
First TWO steps are similar to previous problem.
Note the manner in which side inclination is given.
End A 35 mm above HP & End B is 10 mm above HP.
So redraw 2nd FV as final FV placing these ends as said.

## Slide 22: Plane Inclined to Both RPs
A square lamina of 50 mm side rests on one of the corners on the HP. The diagonal through that corner makes 30o to the VP. The two sides containing this corner make equal inclination with HP. The surface of the lamina makes 45o to the HP. Draw the TV and FV of the lamina.
50
45
45

## Slide 23: Plane Inclined to Both RPs
Problem 10: A square lamina of 50 mm side rests on one of the corners on the HP. The diagonal through that corner makes 30o to the VP. The two sides containing this corner make equal inclination with HP. The surface of the lamina makes 45o to the HP. Draw the TV and FV of the lamina.
X
Y
45
a
b
c
d
a’
b’, d’
c’
45
a1’
b1’
d1’
c1’
a1
b1
c1
d1
AC diagonal is already inclined at 45o to HP. Find apparent angle.
30
a
c
a1
c1
a2
c2
d2
b2
a2’
d2’
c2’
d2’

## Slide 24
450
300
a’
b’1
c’1
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
c1
d1
b’
c’
a’1
d’1
d1
b1
c1
a1
X
Y
300
b’1
c’1
c1
a’1
d’1
d1
b1
c1
a1
450
a’
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
d1
b’
c’
X
Y
TL
Problem 11: A rhombus of diagonals 40 mm and 70 mm long respectively has one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP. If the top-view of the same diagonal makes 400 inclination with VP, draw it’s projections.
Problem 11b: A rhombus of diagonals 40 mm and 70 mm long respectively having one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP and makes 400 inclination with VP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diagonal horizontal? ---------- Longer
Hence begin with TV, draw rhombus below
X-Y line, taking longer diagonal // to X-Y
c2
The difference in these two problems is in step 3 only.
In Problem no. 11, inclination of TV of that diagonal is given. It could be drawn directly as shown in 3rd step.
While in 11b, angle of diagonal itself i.e. it’s TL, is
given. Hence here angle of TL is taken, locus of c1
Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed. Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.
Notes: In the right most views that we draw in any figure , the angle that we draw represents the angle of TV with VP , hence when we have angle of TL with VP as in eg. 11b, we use the knowledge of lec 4 to determine the TV by first drawing the true length with the true angle.
In eg 11, the angle of inclination of the top view is given directly

## Slide 25
a
d
c
b
a’
b’
d’
c’
X
Y
a’
b’
d’
c’
a1
b1
d1
c1
a1
b1
d1
c1
450
300
a’1
b’1
c’1
d’1
Problem 12: A circle of 50 mm diameter is
resting on HP on end A of it’s diameter AC
which is 300 inclined to HP while it’s TV
is 450 inclined to VP. Draw it’s projections.
Problem 12b: A circle of 50 mm diameter is
resting on HP on end A of its diameter AC
which is 300 inclined to HP while it makes
450 inclined to VP. Draw its projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AC
Hence begin with TV, draw circle below
X-Y line, taking the diameter // to X-Y
The difference in these two problems is in step 3 only.
In Problem 12, inclination of TV of that AC is
Given. It could be drawn directly as shown in 3rd step.
While in Problem 12b, angle of AC itself i.e. it’s TL, is
given. Hence here angle of TL is taken, locus of c1
is drawn and then LTV i.e. a1 c1 is marked and
final TV was completed. Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.
a
d
c
b
a’
b’
d’
c’
X
Y
a’
b’
d’
c’
a1
b1
d1
c1
a1
b1
d1
c1
450
300
a’1
b’1
c’1
d’1
c2
a2

## Slide 26
As 3rd step
redraw 2nd TV keeping
side DE on xy line.
Because it is in VP
as said in problem.
X
Y
a
b
c
d
e
f
Repeat: Problem 8:
A hexagonal lamina has its one side in HP and
Its opposite parallel side is 25 mm above HP and
In VP. Draw it’s projections.
Take side of hexagon 30 mm long.
ONLY CHANGE is the manner in which surface inclination
is described:
One side on HP & it’s opposite side 25 mm above HP.
Hence redraw 1st FV as a 2nd FV making above arrangement.
Keep a’b’ on XY & d’e’ 25 mm above XY.
25
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
c1’
b’1
a’1
f’1
d’1
e’1
f1
a1
c1
b1
d1
e1

## Slide 27
Problem 13: End A of diameter AB of a circle is in HP
and end B is in VP. Diameter AB, 50 mm long is
300 & 600 inclined to HP & VP respectively.
Draw projections of circle.
The problem is similar to Problem 12B
But in the 3rd step there is one more change.
Like 9th problem True Length inclination of dia. AB is definitely expected
but if you carefully note - the SUM of it’s inclinations with HP & VP is 900, which
means Line AB lies in a Profile Plane.
Hence it’s both TV & FV must arrive on one single projector. (Similar to Problem 8b)
So do the construction accordingly AND note the case carefully..
SOLVE SEPARATELY
ON DRAWING SHEET
GIVING NAMES TO VARIOUS
POINTS AS USUAL,
AS THE CASE IS IMPORTANT
TL
X
Y
300
600
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AB
Hence begin with TV, draw CIRCLE below
X-Y line, taking dia AB // to X-Y

## Slide 28
Thank You for Patient Hearing