## Slide 1: CE101 Engineering Drawing Lec3: Orthographic Projections
Indian Institute of Technology Guwahati
Notes: Today we will discuss about the Modeling and

## Slide 2
In engineering drawing, the word ‘projection’ means
an image or the act of obtaining the image of an object.
Technical people often refer to the image as a view.
Projection System
Observer or stationary point
Object
Projectors
Plane of projections (POP)

## Slide 3
PROJECTION METHOD
Depending on the relationship between the projectors and POP, and the number of POPs used for the projections, the projection methods are classified as follows

## Slide 4
View comparison
Pictorial drawing
Perspective drawing
Multi-view drawing
Difficult to create
Easy to visualize.
Shape and angle distortion
Object looks more like what our eyes
perceive.
Size and shape distortion
Right angle becomes obtuse angle.
Circular hole becomes ellipse
Distorted
width
Accurately presents object’s details, i.e.
size and shape.
Require training
to visualization.
Advantage
Disadvantage
Type

## Slide 5: Orthographic Projections
Orthographic Projections is a technical drawing in which different views of an object are projected on different reference planes, while observing perpendicular to the respective reference plane.
Different Reference planes (or Principal planes)
  Horizontal Plane (HP)
    Horizontal reference plane (HRP)
  Vertical Plane (VP)
    Frontal reference plane (FRP)
  Side or Profile Plane (PP)
    Profile reference plane (PRP)
Different views are;
  Front View (FV) – Projected on VP
  Top View (TV) – Projected on HP
  Side View (SV) – Projected on PP
FV
TV
SV

## Slide 6
Front View When the observer looks at the object from the front, the view obtained is called the front view (FV) or Elevation. FV is seen on the VP.
  Rear View When the observer looks to the object from back, the view obtained is called rear view (RV) or back view or rear elevation.
Top View When the observer looks at the object from above, the view obtained is called top view (TV) or plan. TV is seen on the HP.
  Bottom View When the observer looks to the object from below, the view obtained is called bottom view (BV) or bottom plan.
Side Views When the observer looks at the object from side, i.e., from his left-hand side or righthand side, the view obtained is called side view (SV). SV is seen on the PP.
  Left-Hand Side View When the observer views the object from his left-hand side, the view obtained is called left-hand side view (LHSV).
  Right Hand Side View When the observer views the object from his right-hand side, the view obtained is called as right-hand side view (RHSV).
The FV, TV and either LHSV or RHSV are usually drawn in orthographic projection. The other views are added if they are extremely essential.

## Slide 7

A.I.P.
 to Vp
&
 to Hp

A.V.P.
 to Hp &  to Vp
PLANES
PRINCIPAL PLANES
HP AND VP
AUXILIARY PLANES
Auxiliary Vertical Plane
(A.V.P.)
Profile Plane
( P.P.)
Auxiliary Inclined Plane
(A.I.P.)

## Slide 8
Multi-view orthographic projections
In this type of projection, we imagine the object being drawn in the center of a transparent box.
The different views of the object are projected onto the sides of this box.

## Slide 9: Multi-view orthographic projections
The projection box and its six views are spread in such a way as to place all the views on the same plane.
The other views pivot around the front view.
BOTTOM VIEW
LEFT SIDE VIEW
REAR VIEW
FRONT VIEW
RIGHT SIDE VIEW
TOP VIEW

## Slide 10: Multi-view orthographic projections
Among the six possible views, we will choose to portray those necessary to the description of the shape of the object.
FRONT VIEW
RIGHT SIDE VIEW
TOP VIEW
LEFT SIDE VIEW
REAR VIEW
BOTTOM VIEW
Three views are usually enough to portray an object. Many simple objects may only require one or two views.

## Slide 11
Projection systems
1. First angle system
2. Third angle system
First
quadrant
Third
quadrant
- European countries - ISO standard
- Canada, USA, Japan, Thailand
Transparent
planes
Opaque
planes

## Slide 12
S.V.
F.V.
V.P.
P.P.
FOR T.V.
FOR S.V.
FOR F.V.
OBJECT
FIRST ANGLE
PROJECTION
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN FIRST QUADRANT
MEANS
ABOVE HP & INFRONT OF VP.
OBJECT IS INBETWEEN
OBSERVER & PLANE.
ACTUAL PATTERN OF
PLANES & VIEWS
IN
FIRST ANGLE METHOD
OF PROJECTIONS
X
Y
VP
HP
PP
FV
LSV
TV

## Slide 13
ACTUAL PATTERN OF
PLANES & VIEWS
OF
THIRD ANGLE PROJECTIONS
X
TV
LSV
FV
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN THIRD QUADRANT
( BELOW HP & BEHIND OF VP. )
PLANES BEING TRANSPERENT
AND INBETWEEN
OBSERVER & OBJECT.
FOR T.V.
FOR S.V.
FOR F.V.
P.P.
V.P.
F.V.
S.V.
OBJECT
Y
THIRD ANGLE
PROJECTION

## Slide 14
1st angle system
(Opaque planes)
3rd angle system
(transparent planes/glass box)
Orthographic views

## Slide 15
Folding
line
Folding
line
Folding
line
Folding
line


1st angle system
3rd angle system
Orthographic views

## Slide 16
1st angle system
3rd angle system
Front View
Front View
Right Side View
Right Side View
Top View
Top View
Views arrangement

## Slide 17
FV

## Slide 19
Projection symbols
1st angle system
3rd angle system
d
1.7d
2.2d

## Slide 20
THIS IS A PICTORIAL SET-UP OF ALL THREE PLANES.
ARROW DIRECTION IS A NORMAL WAY OF OBSERVING THE OBJECT.
BUT IN THIS DIRECTION ONLY VP AND A VIEW ON IT (FV) CAN BE SEEN.
THE OTHER PLANES AND VIEWS ON THOSE CAN NOT BE SEEN.
X
Y
HP IS ROTATED DOWNWARD 900
AND
BROUGHT IN THE PLANE OF VP.
PP IS ROTATED IN RIGHT SIDE 900
AND
BROUGHT IN THE PLANE OF VP.
X
Y
X
Y
VP
HP
PP
FV
ACTUAL PATTERN OF PLANES & VIEWS
OF ORTHOGRAPHIC PROJECTIONS
DRAWN IN
FIRST ANGLE METHOD OF PROJECTIONS
LSV
TV
PROCEDURE TO SOLVE ABOVE PROBLEM:-
TO MAKE THOSE PLANES ALSO VISIBLE FROM THE ARROW DIRECTION,
A) HP IS ROTATED 900 DOUNWARD
B) PP, 900 IN RIGHT SIDE DIRECTION.
THIS WAY BOTH PLANES ARE BROUGHT IN THE SAME PLANE CONTAINING VP.
PATTERN OF PLANES & VIEWS (First Angle Method)

## Slide 21
NOTATIONS
Following notations should be followed while naming
Different views in orthographic projections.
IT’S FRONT VIEW a´ a´ b´
Same system of notations should be followed
incase numbers, like 1, 2, 3 – are used.
OBJECT POINT A LINE AB
IT’S TOP VIEW a a b
IT’S SIDE VIEW a´´ a´´ b´´
TERMS ‘ABOVE’ & ‘BELOW’ WITH RESPECT TO H.P.
AND TERMS ‘INFRONT’ & ‘BEHIND’ WITH RESPECT TO V.P.

## Slide 23
Two dimensions are visible.
What is third dimension?
Another view is required.
Example 1

## Slide 25
Example 2

## Slide 27
Example 2: Reference Line

## Slide 28
Example 2: Reference Line

## Slide 29
If a face is perpendicular to the direction of viewing, its true shape and actual size will be seen in that view.
If a face is parallel to the direction of viewing, it is seen as a line in that view. This view is called the line view or edge view.
If a face is inclined to the direction of viewing, its true shape and size will not be seen in any view.
If an edge of the object is perpendicular to the direction of viewing, its actual length will be seen in that view.
If an edge of the object is parallel to the direction of viewing, it is seen as a point in that view. This view is called point view.
If an edge of the object is inclined to the direction of viewing, its shortened length (projected) will be seen in that view. The shortened length is obtained by locating the end points of the edge.
To obtain the projections of various faces of an object, the following rules must be observed

## Slide 30
Parallel Surfaces
TV
TV

## Slide 31
Inclined Surfaces
h
w
h
w
w
u
u

## Slide 32
Oblique Surfaces

## Slide 33
Curved Surfaces
h
w
u
h
u
u
w

## Slide 34
1. Natural Method: Revolve the object with respect to observer
Methods of Orthogonal Projection
2. Glass box method: The observer moves around the object.
Front view
Right side view
Top view
Right side
view
Top view
play
play
Front
view
Glass box concept

## Slide 35
Glass box : Revolution of the planes of projection
Bottom view
Left side view
Rear view

## Slide 36
Height
Width
Depth
Relative orientation of views
Left side view
Right side view
Bottom view
Top view
Rear view
Front view

## Slide 37
Summary : Problem solving steps
1
2
3
4
Given

## Slide 38
Steps for Orthographic Views
1. Select the necessary views
2. Layout the selected views on a drawing sheet.
3. Complete each selected views.
4. Complete the
dimensions and notes.
45
152
152
64
25~40
Front
Top
Choose a drawing scale
(say 1:1)
Front
Top
y
y
x
x
x
x
y
y
z

## Slide 39
Thank You for Patient Hearing